# A Case Study of Distributing Engineering Services Across the Internet2 Infrastructure

Charles S. Han and Kincho H. Law

Center for Integrated Facility Engineering

Stanford University

Stanford, CA  94305-4020

# Introduction

This paper describes an implementation of distributing engineering services over the Internet2 infrastructure.  Specifically, we compare the run times of a wheelchair analysis of a Stanford University building distributing the engineering analysis over three computer networks:

- The internal Stanford University Network (SUNet).

- The traditional Internet backbone between Stanford and Illinois Institute of Technology (IIT) Main Campus.

- The Internet2 backbone between Stanford and the University of Illinois at Urbana-Champaign (UIUC).

From these comparisons, we gain a better understanding about the strengths and weaknesses of various elements of our implementation choices including the distributed object environment, the distributed analysis architecture, and the wheelchair simulation.  In addition, we discuss the advantages or lack thereof of the Internet2 backbone over the traditional Internet.

# The Distributed Architecture

This study extends the work presented in [1] and [2] that describe an architecture to distribute engineering services over the Internet.  Figure 1 illustrates the three-tiered distributed architecture:

- The first tier consists of a common communication protocol which allows the services to communicate with each other.

- The second tier consists of an optional common product model interface.

- The third tier holds the actual analysis module of the service.

The prototype uses CORBA for its distributed communication protocol, and most of the services are implemented using the Java programming language [3].  Note that services can register with other services to aggregate and form composite services.

Figure 2 shows the implemented services in the prototype.  For this Internet2 exercise, the study focused on the analysis of a Stanford University building for wheelchair accessibility (the Disabled Access Analysis Service shown in the middle of Figure 2).

Figure 3 shows the decomposition of the composite wheelchair analysis service.  The building model is decomposed at each service module by architectural function (building, story, and space), and the leaf service, a motion planner, generates paths among entry points of a space.  The composite service then takes the path segment information and attempts to construct a path through the entire building.  Figure 4 illustrates the calculate path for the Stanford University building between the entrance and a toilet in a bathroom.  This is the path calculated for this study.

# Results

Figure 5 illustrates the distribution of the Disabled Access Analysis Service between Stanford University (SUNet) and the Illinois facilities (IIT for the non-I2 runs and UIUC for the I2 runs).  Before executing and comparing the SUNet-IIT and SUNet-UIUC runs, two preliminary benchmarks were established:

- A traceroute comparison among the machines used for an internal Stanford run of the analysis (ce-556k-pent-1.stanford.edu to ce-556k-sun-1.stanford.edu), the SUNet-IIT path (ce-556k-pent-1.stanford.edu to host54.cae.iit.edu), and the SUNet-UIUC path (ce-556k-pent-1.stanford.edu to ampere-ceg.uiuc.edu) shown in Table 1.

- The execution time of the internal SUNet run of the analysis shown in Table 2.

The comparison between the SUNet-IIT and SUNet-UIUC runs is summarized in the following tables:

- Table 3 shows the SUNet-IIT (non-Internet2 runs)

- Table 4 shows the SUNet-UIUC (Internet2 runs)

- Table 5 compares the averages of all three runs (the SUNet internal run, the SUNet-IIT run, and the SUNet-UIUC run.

As expected and as shown in Table 1, the traceroute time for the internal SUNet path is significantly faster than the SUNet-Illinois runs.  However, the traceroute times for the non-I2 and I2 paths are within about one percent of each other with the I2 path being only slightly faster.  As shown in Table 5 and paralleling the traceroute results, the average execution times of the non-I2 and I2 runs are similar (average times of 2,170 and 2,286 seconds respectively) with both being about twice as slow as the internal SUNet run (1,205 seconds).

# Discussion

For the comparison test outlined in this study, no gain was realized using the Internet2 infrastructure comparing a run with a similar physical distance using the non-Internet2 infrastructure.  The overhead associated with the CORBA distributed object protocol can be ruled out as the overriding bottleneck since the internal SUNet run was twice as fast as the SUNet-Illinois runs.  In addition, the majority of the processing time takes place in the motion planning service, and this service is hosted by an SUNet server in all the runs.

More likely, the overriding bottleneck occurred at the termination points of the SUNet-UIUC run.  From the SUNet side, the 622 megabit Internet2 speeds could not be fully-realized: as shown in Table 1, the traceroute takes three hops along the 100 megabit SUNet infrastructure before reaching the Internet2 gateway.  On the UIUC side, the traceroute leaves the Internet2 backbone and takes four hops along the 10/100BaseT infrastructure.  Thus, the potential six-fold increase in speed along the Internet2 backbone is negated by the bottlenecks at the terminus points.

As demonstrated by this study, to fully-realize the potential speed of the Internet2 infrastructure for distributing engineering analysis services, the complete run between servers must be free of non-Internet2 bottlenecks.

# Acknowledgments

We are deeply indebted to Professor Eduardo de Santiago, Department of Civil and Architectural Engineering at Illinois Institute of Technology, and Professor Narayana R. Aluru, Department of General Engineering, and the Computational Electronics Group at the University of Illinois at Urbana-Champaign for the use of their computational facilities. This research has been funded by the Center for Integrated Facilities Engineering and Information Technology Systems and Services at Stanford University, an equipment grant from Intel Corporation, and continuation funding from the National Science Foundation.

# References

- Han, C.S., Kunz, J.C., and Law, K.H. (1999).  “Building design services in a distributed architecture,” J. Comp. in Civ. Engrg., , ASCE, 13(1), 12-22.

- Han, C.S. (2000). Computer models and methods for a disabled access analysis design environment, Department of Civil and Environmental Engineering, Stanford University.

- Vogel, A., and Duddy, K. (1997).  Java programming with CORBA, John Wiley and Sons, Inc., New York, N.Y.

List of Tables

Table 1: Traceroutes from ce-556k-pent-1.stanford.edu (Internet2 hubs in italics).

Table 2: Internal SUNet Wheelchair Analysis Runs

Table 3: SUNet-IIT Wheelchair Analysis Runs

Table 4: SUNet-UIUC (using Internet2) Wheelchair Analysis Runs

Table 5: Comparison and summary of runs.

List of Figures

Figure 1: The three-tiered distributed service architecture

Figure 2: The prototype services

Figure 2: The distribution of the Disabled Access Analysis services

Figure 4: The calculated wheelchair route

Figure 3: The distribution of services

Table 1: Traceroutes from ce-556k-pent-1.stanford.edu (Internet2 hubs in italics).

Table 2: Internal SUNet Wheelchair Analysis Runs

Table 3: SUNet-IIT Wheelchair Analysis Runs

Table 4: SUNet-UIUC (using Internet2) Wheelchair Analysis Runs

Table 5: Comparison and summary of runs.

Figure 1: The three-tiered distributed service architecture

Figure 2: The prototype services

Figure 3: The distribution of the Disabled Access Analysis services

Figure 4: The calculated wheelchair route

Figure 5: The distribution of services

# Footnotes

Post-doctorate Fellow, Department of Civil and Environmental Engineering, Stanford University, Stanford, CA 94305, csh@stanfordalumni.org

Professor, Department of Civil and Environmental Engineering, Stanford University, Stanford, CA 94305, law@cive.stanford.edu